- Calculate the missing colors and resistors in the following tables..
- In the last column, calculate the current that will flow through the resistor when connected to a 9 volt battery.
- All values should be written to 3 decimal places and with the multiplier symbol that best corres-ponds to it (M=Mega, k=kilo, m=mili, =micro)

COMMERCIAL SERIES E6: (5%)

VALUE 	1st DIGIT	2nd / DIGIT	MULTI-PLIER	TOLE-RANCE		I = 9v / R
4.7 M
	RED	RED	BLACK	GOLD
15 
	ORANGE	ORANGE	GOLD	GOLD
10 k
	BROWN	GREEN	BROWN	GOLD
220 
	YELLOW	VIOLET	BLACK	GOLD
3.3 k
	RED	RED	RED	GOLD
100 
	BLUE	GREY	BROWN	GOLD
22 k
	BROWN	BLACK	YELLOW	GOLD
1.0 
	BLUE	GREY	ORANGE	GOLD
680 k
	ORANGE	ORANGE	GREEN	GOLD

COMMERCIAL SERIES E6: (5%)

VALUE 	1st / DIGIT	2nd / DIGIT	MULTI-PLIER	TOLE-RANCE		I = 9v / R
1.5 k
	YELLOW	VIOLET	RED	GOLD
2.2 
	BROWN	BLACK	BLACK	GOLD
2.2 M
	BROWN	GREEN	ORANGE	GOLD
330 k
	RED	RED	YELLOW	GOLD
4.7 
	BLUE	GREY	GREEN	GOLD
470
	BROWN	BLACK	RED	GOLD
47 k
	BROWN	GREEN	GOLD	GOLD
33 
	BROWN	GREEN	GREEN	GOLD
150 k
	BLUE	GREY	GOLD	GOLD
68 
	ORANGE	ORANGE	BROWN	GOLD
1 M
	ORANGE	ORANGE	ORANGE	GOLD
6.8 k
	YELLOW	VIOLET	YELLOW	GOLD

COLOR	VALUE	MULTI-PLIER	TOLE- / RANCE
BLACK	0	x 1
BROWN	1	x 10	± 1%
RED	2	x 100	± 2%
ORANGE	3	x 1000
YELLOW	4	x 10 000
GREEN	5	x 100 000
BLUE	6	x 1000 000
VIOLET	7
GREY	8
WHITE	9
GOLD		x 0.1	± 5%

RESISTOR COLOR CODES

CC BY-SA 4.0 www.picuino.com

COLOR	VALUE	MULTI-PLIER	TOLE- / RANCE
BLACK	0	x 1
BROWN	1	x 10	± 1%
RED	2	x 100	± 2%
ORANGE	3	x 1000
YELLOW	4	x 10 000
GREEN	5	x 100 000
BLUE	6	x 1000 000
VIOLET	7
GREY	8
WHITE	9
GOLD		x 0.1	± 5%

RESISTOR COLOR CODES

CC BY-SA 4.0 www.picuino.com

COMMERCIAL SERIES E6: (5%)

VALUE / 	1st / DIGIT	2nd / DIGIT	MULTI-PLIER	TOLE-RANCE		I = 9v / R
1.5 k	BROWN	GREEN	RED	GOLD		6,00 mA
4.7 k	YELLOW	VIOLET	RED	GOLD		1,91 mA
2.2 	RED	RED	GOLD	GOLD		4,09 A
10 	BROWN	BLACK	BLACK	GOLD		900 mA
2.2 M	RED	RED	GREEN	GOLD		4,09 A
15 k	BROWN	GREEN	ORANGE	GOLD		600 A
330 k	ORANGE	ORANGE	YELLOW	GOLD		27,3 A
220 k	RED	RED	YELLOW	GOLD		40,9 A
4.7 	YELLOW	VIOLET	GOLD	GOLD		1,91 A
6.8 M	BLUE	GREY	GREEN	GOLD		1,32 A
470	YELLOW	VIOLET	BROWN	GOLD		19,2 mA
1 k	BROWN	BLACK	RED	GOLD		9,00 mA
47 k	YELLOW	VIOLET	ORANGE	GOLD		192 A
1.5 	BROWN	GREEN	GOLD	GOLD		6,00 A
33 	ORANGE	ORANGE	BLACK	GOLD		273 mA
1.5 M	BROWN	GREEN	GREEN	GOLD		6,00 A
150 k	BROWN	GREEN	YELLOW	GOLD		60,0 A
6.8 	BLUE	GREY	GOLD	GOLD		1,32 A
68 	BLUE	GREY	BLACK	GOLD		132 mA
330 	ORANGE	ORANGE	BROWN	GOLD		27,3 mA
1 M	BROWN	BLACK	GREEN	GOLD		9,00 A
33 k	ORANGE	ORANGE	ORANGE	GOLD		273 A
6.8 k	BLUE	GREY	RED	GOLD		1,32 mA
470 k	YELLOW	VIOLET	YELLOW	GOLD		19,2 A

- Calculate the missing colors and resistors in the following tables..
- In the last column, calculate the current that will flow through the resistor when connected to a 9 volt battery.
- All values should be written to 3 decimal places and with the multiplier symbol that best corres-ponds to it (M=Mega, k=kilo, m=mili, =micro)

COMMERCIAL SERIES E6: (5%)

VALUE / 	1st / DIGIT	2nd / DIGIT	MULTI-PLIER	TOLE-RANCE		I = 9v / R
4.7 M	YELLOW	VIOLET	GREEN	GOLD		1,91 A
22 	RED	RED	BLACK	GOLD		409 mA
15 	BROWN	GREEN	BLACK	GOLD		600 mA
3.3 	ORANGE	ORANGE	GOLD	GOLD		2,73 A
10 k	BROWN	BLACK	ORANGE	GOLD		900 A
150 	BROWN	GREEN	BROWN	GOLD		60,0 mA
220 	RED	RED	BROWN	GOLD		40,9 mA
47 	YELLOW	VIOLET	BLACK	GOLD		192 mA
3.3 k	ORANGE	ORANGE	RED	GOLD		2,73 mA
2.2 k	RED	RED	RED	GOLD		4,09 mA
100 	BROWN	BLACK	BROWN	GOLD		90,0 mA
680 	BLUE	GREY	BROWN	GOLD		13,2 mA
22 k	RED	RED	ORANGE	GOLD		409 A
100 k	BROWN	BLACK	YELLOW	GOLD		90,0 A
1.0 	BROWN	BLACK	GOLD	GOLD		9,00 A
68 k	BLUE	GREY	ORANGE	GOLD		132 A
680 k	BLUE	GREY	YELLOW	GOLD		13,2 A
3.3 M	ORANGE	ORANGE	GREEN	GOLD		2,73 A